## Slide 1: Self Balancing Robot
-by Abhishek Ghogare (153059006)

## Slide 2: Problem Statement
Robot balances itself by moving in 1 dimension
Accelerometer/Gyro sensor detects the direction of fall
Microcontroller receives sensor data and acts on motors connected to wheels
Microcontroller should track the movement of the robot to maintain the its position

## Slide 3: Task specifications
I2C protocol communication for MPU
Calculate bot angle with minimum noise
  Calculate and smooth angle using only accelerometer
    Use tan angle instead of sin to avoid max length calculation and error minimization
  Integrate angular velocity over time to get angle
    Two reasons to drift the angle
      Non zero sensor output in steady state
      Accumulation of error due to integration over time
  Complementary filter, to fuse both angles
Use PID to balance bot
Quadrature encoder for position tracking
Quadrature encoder for speed tracking

## Slide 4: MPU-9250 Communication
Two communication protocols to interact with MPU
  SPI
    Simple protocol
    Pins : SCLK, MOSI, MISO, SS
  I2C
    Supports multi master-slave on same bus
    Pins : SCL, SDA
Used I2C module and library from Tiva Launchpad

## Slide 5: Bot angle calculation Accelerometer
Very noisy even in steady state

## Slide 6: Bot angle calculation Accelerometer
Using simple median filter decreased much noise
  Uses 10 last samples

## Slide 7: Bot angle calculation Accelerometer
Using tan(α) instead of cos(α)
Two advantages
  Excludes max value of accelerometer from consideration
  Minimizes error by considering multiple axes
Angle does not drift, so good reference point
Z acc
X acc
tan α =

## Slide 8: Bot angle calculation Gyroscope
Integration over time
Very smooth, less noise
Calculated angle drifts over time
  Since error in sensor data also get integrated
  Non-zero offset of the sensor output
  Sensor sensitivity is not constant

## Slide 9: Bot angle calculation Gyroscope
X
Y
Z

## Slide 10: Bot angle calculation Accelerometer + Gyroscope
What is the solution?
Complementary filter
  x x τ x

## Slide 11: Bot angle calculation Accelerometer + Gyroscope
Acc angle
Filtered angle

## Slide 12: PID Controller
-
Sensor Output
Set Point
+
Error
Actuator
: Proportional term
: Integral term
: Derivative term

## Slide 13: PID Controller
-
Measured angle
Angle offset
+
Error
Motor PWM
: Proportional term
: Integral term
: Derivative term

## Slide 14: PID Controller
Problem
  Unstable bot even after PID tuning
Solution
  Added offset to PWM values for each motor by measuring
Problem
  Bot angle stabilizes, but not the position
Solution
  Cascade position PID, add output of position PID to set point of angle PID
Another problem
  Bot tries to stabilize position and angle both, but does not maintain the speed
Solution
  Add another PID for speed control, add output of speed PID to set point of angle PID
+
Angle PID
Angle Offset
+
Angle PID
Angle Offset
Position PID
+
Position PID
Angle PID
Angle Offset
Speed PID

## Slide 15: Cascaded PID
+
Position PID
Angle PID
Angle Offset
Speed PID
Add position PID output to set point of angle PID
Position tries to stabilize but speed not
So, add speed PID output to set point of angle PID
One advantage is no need to add angle offset since position PID compensate for that

## Slide 16: Future Enhancements
Directly use target speed PID to achieve desired motor speed
  So, no need to add PWM offset to motors
Use onboard DMP to offload MPU value processing
Both encoder integration
Remote control
Height independent PIDs

## Slide 17: Metrics
Single iteration runs in 14ms
Execution time should not be less than 10ms, it introduces velocity calculation errors

## Slide 18: Hardware Modules
Tiva Launchpad
  I2C module for MPU communication
  Quadrature encoder module for motor encoder
    Two modules
    Acceptable input frequency is of the processor frequency
    Direction change detection

## Slide 19: Software Modules
PID controller library
Median filter
Complementary filter

## Slide 20: Connections Diagram

## Slide 21: Project Timeline
Checkpoint | Date
MPU testing with Tiva Launchpad | 07 Oct 2016
Robot connection and basic motor movement | 09 Oct 2016
Angle measurement using accelerometer | 11 Oct 2016
Angle calculation using gyroscope | 11 Oct 2016
Sensor fusion using complementary filter | 12 Oct 2016
PID controller integration | 14 Oct 2016
Quadrature encoder module to track position | 16 Oct 2016
Position PID integration | 17 Oct 2016
Motor speed calculation and Speed PID integration | 19 Oct 2016
Another layer of speed PID to achieve desired speed | 23 Oct 2016